## Slide 1
H.E.L.I.O.S.
Helium
Exhaust
Liberating
Inflation
Optimization
System

## Slide 2: Mission Description
To create a payload with which we can release a certain amount of helium from the balloon in order to manage the balloon and its payloads’ ascent

## Slide 3: H.E.L.I.O.S. Payload
Made of two parts: the wheel plug and the actual payload
Uses a GPS and a pressure sensor to determine the altitude and position
When an appropriate height/pressure is reached, the valve will open
The valve stays open for a period of time and then shuts again
All data is logged for study at a later date

## Slide 4: Wheel Plug
Sits inside the neck of the balloon → where latex is the thickest
Payloads will hang from crossbar, by cord
1” diameter hole for valve tubing to run through
~1kg

## Slide 5: Balloon Payload
Contains Arduino Uno, Gardena Irrigation Valve, circuitry, batteries, tubing, and pressure sensors.
Made with posterboard and insulation → 7” cube
Hangs directly below the wheel plug
~0.5 kg mass → excluding wheel plug’s mass